## Slide 1
Chapter 2 – Combinational Digital Circuits
Part 2 – Circuit Optimization

## Slide 2: Overview
Part 1 – Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Part 2 – Circuit Optimization
  Two-Level Optimization
Part 3 – Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates

## Slide 3: Circuit Optimization
Goal: To obtain the simplest implementation for a given function
Optimization is a more formal approach to simplification that is performed using a specific procedure or algorithm
Optimization requires a cost criterion to measure the simplicity of a circuit
Distinct cost criteria we will use:
  Literal cost (L)
  Gate input cost (G)
  Gate input cost with NOTs (GN)

## Slide 4: Literal Cost
D
Literal – a variable or its complement
Literal cost – the number of literal appearances in a Boolean expression corresponding to the logic circuit diagram
Examples:
  F = BD + A C + A L = 8
  F = BD + A C + A + AB L =
  F = (A + B)(A + D)(B + C + )( + + D) L =
  Which solution is the best?
D
B
C
B
B
D
C
B
C
Notes: 2nd Literal Cost = 11
3rd Literal Cost = 10
The first solution is best

## Slide 5: Gate Input Cost
Gate input costs - the number of inputs to the gates in the implementation corresponding exactly to the given equation or equations. (G - inverters not counted, GN - inverters counted)
For SOP and POS equations, it can be found from the equation(s) by finding the sum of:
  all literal appearances
  the number of terms excluding single literal terms,(G) and
  optionally, the number of distinct complemented single literals (GN).
Example:
  F = BD + A C + A G = 11, GN = 14
  F = BD + A C + A + AB G = , GN =
  F = (A + )(A + D)(B + C + )( + + D) G = , GN =
  Which solution is the best?
D
B
C
B
B
D
C
B
D
B
C
Notes: G = 15, GN = 18 (second value includes inverter inputs)
G = 14, GN = 17
1st solution is best

## Slide 6: Cost Criteria (continued)
Example 1:
F = A + B C +
A
B
C
F
B
C
L = 5
L (literal count) counts the AND inputs and the single literal OR input.
G = L + 2 = 7
G (gate input count) adds the remaining OR gate inputs
GN = G + 2 = 9
GN(gate input count with NOTs) adds the inverter inputs

## Slide 7: Cost Criteria (continued)
Example 2:
F = A B C +
L = 6 G = 8 GN = 11
F = (A + )( + C)( + B)
L = 6 G = 9 GN = 12
Same function and same literal cost
But first circuit has better gate input count and better gate input count with NOTs
Select it!
B
C
A
A
B
C
F
C
B
F
A
B
C
A

## Slide 8: Boolean Function Optimization
Minimizing the gate input (or literal) cost of a (a set of) Boolean equation(s) reduces circuit cost.
We choose gate input cost.
Boolean Algebra and graphical techniques are tools to minimize cost criteria values.
Some important questions:
  When do we stop trying to reduce the cost?
  Do we know when we have a minimum cost?
Methods
  Quine-McCluskey
  Karnaugh (K-) map
  Espresso

## Slide 9: Optimization Example
f(x1,x2,x3,x4)=m(1,3,5,6,7,8,12,14,15)
f(x1,x2,x3,x4)=x1x2x3x4+x1x2x3x4+ x1x2x3x4+x1x2x3x4+x1x2x3x4+x1x2x3x4
+x1x2x3x4+x1x2x3x4+x1x2x3x4
x1x2x4(x3+x3)
f(x1,x2,x3,x4)=
+x1x3x4(x2+x2)
+x1x3x4(x2+x2)
+x1x2x4(x3+x3)
+x1x2x3(x4+x4)
+x2x3x4(x1+x1)
+x1x2x4(x3+x3)
+x2x3x4(x1+x1)
+x1x2x3(x4+x4)
f(x1,x2,x3,x4)=
x1x2x4
+x1x3x4
+x1x3x4
+x1x2x4
+x1x2x3
+x2x3x4
+x1x2x4
+x2x3x4
+x1x2x3
f(x1,x2,x3,x4)=
x1x4
+x1x4
+x2x3
+x2x3
f(x1,x2,x3,x4)=
x1x4
+x2x3
+x1x3x4(x2+x2)
+x1x3x4
+x1x3x4
+x1x3x4
+x1x2x4
+x1x2x4

## Slide 10: Quine-McCluskey Method
The Boolean function is represented in SOP or POS.
1st Phase: Finding the prime implicants of f.
2nd Phase: Finding optimal representation of f by taking some of the prime implicants.

## Slide 11: Optimization of SOP Representation By Quine-McCluskey Method – 1st Phase : Finding the prime implicants
Example: f(x1,x2,x3,x4)=m(1,3,5,6,7,8,12,14,15)
x1 x2 x3 x4
0 0 0 1
1
8
1 0 0 0
5
0 1 0 1
12
1 1 0 0
7
0 1 1 1
x1 x2 x3 x4
1,5
0 - 0 1
5,7
0 1 - 1




3,7
0 - 1 1
8,12
1 - 0 0

12,14
1 1 - 0

A
B
C
D
Sum of Prime Implicants:
f(x1,x2,x3,x4)=x1x3x4+x1x2x4+x1x4+x2x3
3
0 0 1 1
6
0 1 1 0
1 1 1 0
14
15
1 1 1 1
1,3
0 0 - 1
6,7
0 1 1 -
6,14
- 1 1 0
7,15
- 1 1 1
14,15
1 1 1 -
1,3,5,7
0 - - 1
1,5,3,7
0 - - 1
6,7,14,15
- 1 1 -
6,14,7,15
- 1 1 -
x1 x2 x3 x4












## Slide 12: Optimization of SOP Representation By Quine-McCluskey Method – 2nd Phase : Finding optimal representation
EPI
EPI
EPI
Optimal Representation:
f(x1,x2,x3,x4)=x1x3x4+x1x4+x2x3
A 8,12
B 12,14
C 1,3,5,7
D 6,7,14,15
1
3
5
6
7
8
12
A
B
C
D
X
X
X
X
X
X
X
X
X
X
14
15
X
X
Coverage Table Method

## Slide 13: Optimization of SOP Representation By Quine-McCluskey Method – 2nd Phase : Finding optimal representation
Optimal Representation:
f(x1,x2,x3,x4)=x1x3x4+x1x4+x2x3
A 8,12
B 12,14
C 1,3,5,7
D 6,7,14,15
Petrick’s Method
P=C C C D (C+D) A (A+B) (B+D) D
C=1, D=1, A=1
P=1

## Slide 14: Example: f(x1,x2,x3,x4)=m(1,4,5,7,8,9,11,12,14,15)
x1 x2 x3 x4
0 0 0 1
1
4
0 1 0 0
5
0 1 0 1
12
1 1 0 0
7
0 1 1 1
x1 x2 x3 x4
1,5
0 - 0 1
8,9
1 0 0 -




4,12
- 1 0 0
4,5
0 1 0 -

9,11
1 0 - 1

A
B
C
D
11
1 0 1 1
9
1 0 0 1
1 1 1 0
14
15
1 1 1 1
1,9
- 0 0 1
8,12
1 - 0 0
5,7
0 1 - 1
12,14
1 1 - 0
7,15
- 1 1 1




8
1 0 0 0
11,15
1 - 1 1
14,15
1 1 1 -
E
F
G
H
I
J
K
L
Sum of Prime Implicants:
f(x1,x2,x3,x4)=x1x3x4+x2x3x4+x1x2x3+x2x3x4+x1x2x3+x1x3x4+x1x2x4+x1x2x4+x1x2x4+x2x3x4+x1x3x4+x1x2x3

## Slide 15: Example: f(x1,x2,x3,x4)=m(1,4,5,7,8,9,11,12,14,15)
1
4
5
7
8
9
11
A
B
C
D
X
X
X
X
X
X
X
12
14
X
E
F
G
H
I
J
K
L
15
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
Let A=1
P=(A+B)(C+D)(A+C+G)(G+J)(E+F)
(B+E+H)(H+K)(D+F+I)(I+L)(J+K+L)
None of the rows cover another row.
None of the columns cover another column.
There is no essential prime implicant.
P= (C+D)(G+J)(E+F)(B+E+H)(H+K)
(D+F+I)(I+L)(J+K+L)
There is no essential prime implicant.
E covers B. D covers C. J covers G.
B=0, C=0, G=0
P= D J (E+F)(E+H)(H+K)(D+F+I)(I+L)
(J+K+L)
D and J are essential prime implicants.
D=1, J=1
P= (E+F)(E+H)(H+K)(I+L)
There is no essential prime implicant.
E covers F. H covers K. F=0, K=0
P= E (E+H) H (I+L)
E and H essential prime implicant.
E=1, H=1
There is no essential prime implicant.
No row or column coverage.
I=1 or L=1

## Slide 16: Example: f(x1,x2,x3,x4)=m(1,4,5,7,8,9,11,12,14,15)
Optimal Representation:
f(x1,x2,x3,x4)=x1x3x4+x2x3x4+x2x3x4+x1x2x3+x1x2x4+x1x2x4 or x1x2x3

## Slide 17: Optimization of POS Representation By Quine-McCluskey Method
Example: f(x1,x2,x3,x4)=M(1,4,5,8,11,12,14)
x1 x2 x3 x4
0 0 0 1
1
4
0 1 0 0
8
1 0 0 0
5
0 1 0 1
12
1 1 0 0
11
1 0 1 1
14
1 1 1 0
x1 x2 x3 x4
1,5
0 - 0 1


4,12
- 1 0 0


4,5
0 1 0 -
8,12
1 - 0 0

12,14
1 1 - 0

A
B
C
D
E
F
Product of Prime Implicants:
f(x1,x2,x3,x4)=(x1+x2+x3+x4)
(x1+x3+x4)(x1+x2+x3)(x2+x3+x4)
(x1+x3+x4)(x1+x2+x4)
1
4
8
5
12
11
14
A
B
C
D
E
F
X
X
X
X
X
X
X
X
X
X
X
EPI
EPI
EPI
EPI
Optimal Representation:
f(x1,x2,x3,x4)=(x1+x2+x3+x4)(x1+x3+x4)
(x1+x3+x4)(x1+x2+x4)
(x1+x2+x3) or (x2+x3+x4)

## Slide 18: Optimization of SOP Representation By Quine-McCluskey Method with Don’t Care Conditions
Example: f(x1,x2,x3)=m(0,1,5)+dm(2,6)
Sum of Prime Implicants:
f(x1,x2,x3)=x1x2+x1x3+x2x3+x2x3
0
1
5
A
B
C
X
X
Optimal Representation:
f(x1,x2,x3)=x2x3+x1x2 or
x2x3+ x1x3
x1 x2 x3
0 0 0
0
1
0 0 1
2
0 1 0
5
1 0 1
6
1 1 0
x1 x2 x3
0,1
0 0 -


1,5
- 0 1


0,2
0 - 0
2,6
- 1 0

A
B
C
D
X
X
X
EPI

## Slide 19: Karnaugh Maps (K-map)
A K-map is a collection of squares
  Each square represents a minterm
  The collection of squares is a graphical representation of a Boolean function
  Adjacent squares differ in the value of one variable
  Alternative algebraic expressions for the same function are derived by recognizing patterns of squares
The K-map can be viewed as
  A reorganized version of the truth table
  A topologically-warped Venn diagram as used to visualize sets in algebra of sets

## Slide 20: Some Uses of K-Maps
Provide a means for:
  Finding optimum or near optimum
    SOP and POS standard forms, and
    two-level AND/OR and OR/AND circuit implementations
  for functions with small numbers of variables
  Visualizing concepts related to manipulating Boolean expressions, and
  Demonstrating concepts used by computer-aided design programs to simplify large circuits

## Slide 21: Two Variable Karnaugh Map
Two variable: x ve y
  4 minterms:
    m0 = x’y’  00
    m1 = x’y  01
    m2 = xy’  10
    m3 = xy  11
y x | 0 | 1
0 | m0 | m1
1 | m2 | m3
y x | 0 | 1
0 | x’y’ | x’y
1 | xy’ | xy

## Slide 22: K-Map and Truth Tables
The K-Map is just a different form of the truth table.
Example – Two variable function:
  We choose a,b,c and d from the set {0,1} to implement a particular function, F(x,y).
Function Table
K-Map
Input
Values
(x,y)
Function
Value
F(x,y)
0 0
a
0 1
b
1 0
c
1 1
d
y = 0
y = 1
x = 0
a
b
x = 1
c
d

## Slide 23: K-Map Function Representation
Example: F(x,y) = x
For function F(x,y), the two adjacent cells containing 1’s can be combined using the Minimization Theorem:
x
y
x
y
x
)
y
,
x
(
F
=
+
=
y x | 0 | 1
0 | 0 | 0
1 | 1 | 1

## Slide 24: K-Map Function Representation
Example: G(x,y) = x + y
For G(x,y), two pairs of adjacent cells containing 1’s can be combined using the Minimization Theorem:
(
)
(
)
y
x
y
x
xy
y
x
y
x
)
y
,
x
(
G
+
=
+
+
+
=
Duplicate x y
y x | 0 | 1
0 | 0 | 1
1 | 1 | 1

## Slide 25: Three Variable Karnaugh Map
Note that if the binary value for an index differs in one bit position, the minterms are adjacent on the K-Map
  m2  m6 , m3  m7
  m2  m0 , m6  m4
yz x | 00 | 01 | 11 | 10
0 | m0 | m1 | m3 | m2
1 | m4 | m5 | m7 | m6

## Slide 26: Three Variable Karnaugh Map
Rectengular examples with 2 cells
Read the terms shown by the rectengulars.
0
1
3
2
5
6
4
7
z
y
x
00
01
11
10
0
1

## Slide 27: Three Variable Karnaugh Map
0
1
3
2
5
6
4
7
x
z
y
x
00
01
11
10
0
1
Rectengular examples with 4 cells
Read the terms shown by the rectengulars.

## Slide 28: Example: F(x,y,z)=m(1,2,3,5,7)
z
y
x
00
01
11
10
0
1
1
1
1
1
1
0
0
0
0 1 0
1. col
0 1 1
1 1 1
x y z
2. col
3. col
x y z

0 1 -

- 1 1

1 - 1
0 0 1
0 - 1
- 0 1


- - 1


x y z


A
B
P=AB
A=B=1
A=x’y
B=z
F=A+B=x’y+z
z
x’y
F=x’y+z
1 0 1

## Slide 29: Example: Three Variable Karnaugh Map
F1(x, y, z) =  (2, 3, 4, 5)
1
1
1
1
0
0
0
0
1
0
10
11
01
00
yz
x
F1(x, y, z) = xy’ + x’y
F2(x, y, z) =  (3, 4, 6, 7)
yz x | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 1 | 1
F1(x, y, z) = xz’ + yz

## Slide 30: Example
F1(x, y, z) =  (0, 2, 4, 5, 6)
1
1
1
1
0
0
0
1
z
1
0
10
11
01
00
yz
x
y
x
F1(x, y, z) =z+yx

## Slide 31: Combining Squares
By combining squares, we reduce number of literals in a product term, reducing the literal cost, thereby reducing the other two cost criteria
On a 3-variable K-Map:
  One square represents a minterm with three variables
  Two adjacent squares represent a product term with two variables
  Four “adjacent” terms represent a product term with one variable
  Eight “adjacent” terms is the function of all ones (no variables) = 1.

## Slide 32: Three-Variable Maps
Reduced literal product terms for SOP standard forms correspond to rectangles on K-maps containing cell counts that are powers of 2.
Rectangles of 2 cells represent 2 adjacent minterms; of 4 cells represent 4 minterms that form a “pairwise adjacent” ring.
Rectangles can contain non-adjacent cells as illustrated by the “pairwise adjacent” ring above.

## Slide 33: Three-Variable Map Simplification
Use a K-map to find an optimum SOP equation for
Notes: F = Z’ + X’ Y’ + X Y

## Slide 34: Four Variable Karnaugh Map
4 variables: x, y, z, t
  16 minterms
zt xy | 00 | 01 | 11 | 10
00 | m0 | m1 | m3 | m2
01 | m4 | m5 | m7 | m6
11 | m12 | m13 | m15 | m14
10 | m8 | m9 | m11 | m10
z
t
x
y

## Slide 35: Four Variable Terms
Four variable maps can have rectangles corresponding to:
  A single 1 = 4 variables, (i.e. Minterm)
  Two 1s = 3 variables,
  Four 1s = 2 variables
  Eight 1s = 1 variable,
  Sixteen 1s = zero variables (i.e. Constant "1")

## Slide 36: Four-Variable Maps
Example Shapes of Rectangles:
8
9
10
11
12
13
14
15
0
1
3
2
5
6
4
7
X
Y
Z
W

## Slide 37: Four-Variable Maps
Example Shapes of Rectangles:
X
Y
Z
8
9
10
11
12
13
14
15
0
1
3
2
5
6
4
7
W

## Slide 38: Example: F(x,y,z,t) =  (0, 1, 2, 4, 5, 6, 8, 9, 12, 13, 14)
0
0
0
0
0
10
11
01
00
10
11
01
00
zt
xy
F(x,y,z,t) =
1
1
1
1
1
1
1
1
1
1
1
+yt’
+x’t’
z’

## Slide 39: Example: F(x,y,z,t)=x’y’z’+y’zt’+x’yzt’+xy’z’
10
11
01
1
0
1
1
0
0
0
0
1
0
0
0
1
0
1
1
00
10
11
01
00
zt
xy
F(x,y,z,t) =y’t’+z’y’+x’zt’

## Slide 40: Optimization of POS Representation with Karnaugh Map
Example: f(x,y,z,t)=M(1,4,5,8,11,12,14)
10
11
01
1
0
1
0
0
1
1
0
1
1
0
0
1
1
0
1
00
10
11
01
00
zt
xy
f(x1,x2,x3,x4)=
(x+z+t)
(x+y+t)
(x+z+t)
(x+y+z+t)
(x+y+z) or (y+z+t)

## Slide 41: Systematic Simplification
A Prime Implicant is a product term obtained by combining the maximum possible number of adjacent squares in the map into a rectangle with the number of squares a power of 2.
A prime implicant is called an Essential Prime Implicant if it is the only prime implicant that covers (includes) one or more minterms.
Prime Implicants and Essential Prime Implicants can be determined by inspection of a K-Map.
A set of prime implicants "covers all minterms" if, for each minterm of the function, at least one prime implicant in the set of prime implicants includes the minterm.

## Slide 42: Five Variable or More K-Maps
For five variable problems, we use two adjacent K-maps.
It becomes harder to visualize adjacent minterms for selecting PIs.
You can extend the problem to six variables by using four K-Maps
5 variable  32 cells
xyz tw | 000 | 001 | 011 | 010 | 110 | 111 | 101 | 100
00 | m0 | m4 | m12 | m8 | m24 | m28 | m20 | m16
01 | m1 | m5 | m13 | m9 | m25 | m29 | m21 | m17
11 | m3 | m7 | m15 | m11 | m27 | m31 | m23 | m19
10 | m2 | m6 | m14 | m10 | m26 | m30 | m22 | m18

## Slide 43: Five Variable K-Maps
tw yz | 00 | 01 | 11 | 10
00 | m0 | m1 | m3 | m2
01 | m4 | m5 | m7 | m6
11 | m12 | m13 | m15 | m14
10 | m8 | m9 | m11 | m10
tw yz | 00 | 01 | 11 | 10
00 | m16 | m17 | m19 | m18
01 | m20 | m21 | m23 | m22
11 | m28 | m29 | m31 | m30
10 | m24 | m25 | m27 | m26
x = 0
x = 1
Adjacent:
  A cell in x = 0 map is adjacent to the same cell in x = 1 map.
  Example, m4  m20 and m15  m31 are adjacent.

## Slide 44: Example: Five Variable K-Maps
F(x, y, z, t, w) =  (0, 2, 4, 6, 9, 13, 21, 23, 25, 29, 31)
tw yz | 00 | 01 | 11 | 10
00 | 1 |  |  | 1
01 | 1 |  |  | 1
11 |  | 1 |  | 
10 |  | 1 |  | 
tw yz | 00 | 01 | 11 | 10
00 |  |  |  | 
01 |  | 1 | 1 | 
11 |  | 1 | 1 | 
10 |  | 1 |  | 
x = 0
x = 1
F(x,y,z,t,w) =

## Slide 45: Don't Cares in K-Maps
Sometimes a function table or map contains entries for which it is known:
  the input values for the minterm will never occur, or
  The output value for the minterm is not used
In these cases, the output value need not be defined
Instead, the output value is defined as a “don't care”
By placing “don't cares” ( an “x” entry) in the function table or map, the cost of the logic circuit may be lowered.
Example 1: A logic function having the binary codes for the BCD digits as its inputs. Only the codes for 0 through 9 are used. The six codes, 1010 through 1111 never occur, so the output values for these codes are “x” to represent “don’t cares.”

## Slide 46: Don't Cares in K-Maps
Example 2: A circuit that represents a very common situation that occurs in computer design has two distinct sets of input variables:
  A, B, and C which take on all possible combinations, and
  Y which takes on values 0 or 1.
and a single output Z. The circuit that receives the output Z observes it only for combinations of A, B, and C such that A = 1 and B = 1 or C = 0, otherwise ignoring it. Thus, Z is specified only for those combinations, and for all other combinations of A, B, and C, Z is a don’t care. Specifically, Z must be specified for AB + C = 1, and is a don’t care for :
AB + C = (A + B)C = AC + BC
Ultimately, each don’t care “x” entry may take on either a 0 or 1 value in resulting solutions
For example, an “x” may take on value “0” in an SOP solution and value “1” in a POS solution, or vice-versa.
Any minterm with value “x” need not be covered by a prime implicant.

## Slide 47: Example: BCD “5 or More”
The map below gives a function F1(w,x,y,z) which is defined as "5 or more" over BCD inputs. With the don't cares used for the 6 non-BCD combinations:
        F1 (w,x,y,z) = w + x z + x y G = 7
        This is much lower in cost than F2 where the “don't cares” were treated as "0s."
        G = 12
z
w
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
1
1
1
1
1
X
X
X
X
X
X
0
0
0
0
0
x
y
y
x
w
y
x
w
z
x
w
z)
y,
x,
F2(w,
+
+
=

## Slide 48: Product of Sums Example
Find the optimum POS solution:
Notes: F' = B' D' + A' B
F = (B + D)(A + B')

## Slide 49: Optimization Algorithm
Find all prime implicants.
Include all essential prime implicants in the solution
Select a minimum cost set of non-essential prime implicants to cover all minterms not yet covered:
  Obtaining an optimum solution: See Reading Supplement - More on Optimization
  Obtaining a good simplified solution: Use the Selection Rule

## Slide 50: Prime Implicant Selection Rule
Minimize the overlap among prime implicants as much as possible. In particular, in the final solution, make sure that each prime implicant selected includes at least one minterm not included in any other prime implicant selected.