## Slide 1: Sequential Circuit Model
Combinational Circuit
inputs
outputs
Storage Elements
Present state
Next state
Present state depends on the inputs and previous state

## Slide 2: Synchronous Sequential Circuits
Behavior defined from knowledge of its signals at discrete instances of time.
Discrete instances of time need synchronization.
Synchronization is done by a common clock signal.
Clock signal is a periodic square signal.
  Storage elements observe inputs and can change state only in relation to a timing signal (clock pulses from a clock)

## Slide 3: Synchronous Sequential Circuits
The storage elements are flip-flops that can store one bit of information.
Combinational Circuit
Flip-Flops
inputs
outputs
Present state
Next state
clock

## Slide 4: Latch
Basic storage element
A latch is a storage element that can store its content forever.
Latches are asynchronous circuits and do not need a clock signal to operate.
Hence they can not be used in synchronous circuits directly.
They are used to construct flip-flops.

## Slide 5: SR-Latch
S
Q1
R
Q2
Q1 = (S Q2)’ = S’ + q2’
Q2 = (R Q1)’ = R’ + q1’
S | R | q1 | q2 | Q1 | Q2
0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0
SR=00  00-11-11-…
SR=01  00-11-10-10-…
01-11-11-…
10-11-11-…
} Q1Q2=11
01-11-10-10-…
} Q1Q2=10
SR=10  00-11-01-01-…
10-11-01-01-…
} Q1Q2=01
SR=11  00-11-00-11-…
01-01-…
} Q1Q2=oscilates
10-10-…
} Q1Q2=q1q2

## Slide 6: SR-Latch
S
Q1
R
Q2
S | R | Q1 | Q2
0 | 0 | x | x
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | q | q’
Undefined
6
Q1= Q2’
Q1= Q
Q2= Q ’

## Slide 7: SR-Latch
R
Q
S
Q’
S | R | Q | Q
0 | 0 | q | q
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | X | X
Undefined
Q = (R + Q’)’ = R’ q
Q’ = (S + Q)’ = S’ q’

## Slide 8: Simulation of SR-Latch

## Slide 9: SR-Latch with Control Input
Q
Q’
R
S
C
C | S | R | Q | Q’
0 | X | X | No change | 
1 | 0 | 0 | No change | 
1 | 0 | 1 | Q = 0 | Reset state
1 | 1 | 0 | Q = 1 | Set state
1 | 1 | 1 | Undefined | 
Q= ((S C)’Q’)’=SC + Q
Q’= ((R C)’Q)’=RC + Q’

## Slide 10: Simulation of SR-Latch with Control Input

## Slide 11: D-Latch
Because the undefined situation can cause stability problems, SR latches are not used often.
Solution: D-latch
R
Q
S
Q’
This circuit garanties that S and R inputs are always each other’s complement.
C
D

## Slide 12
Simulation of D-Latch

## Slide 13: D-Latch
D input is sampled when C=1.
C | D | Next state of Q
0 | X | No change
1 | 0 | Q = 0; reset state
1 | 1 | Q = 1; set state
S
R
Q
Q’
SR-latch
D
C
Q
Q’
D-latch

## Slide 14: D Latch as a Storage Element
When C = 1 D latch copies the input to the output.
When C = 0 the information is kept unchanged.
Latches are called level triggered.
  While C is in logic-1 level, the changes at the input cause changes at the output.
The states of the storage elements should change synchronously.
We need a storage element which changes the state in a very short time spot.
These storage elements are called edge triggered and specially flip-flops.

## Slide 15: Edge Triggered D Flip-Flop
Edge triggered D flip-flop can be constructed by using two D latches.
D latch
(master)
D
C
Q
D latch
(slave)
D
C
Q
clk
D
Q
Y
clk’
Q = Y = D
Y = D
clk
Y does not change
Falling edge triggered
D flip-flop
clk’

## Slide 16: Rising Edge Triggered D Flip-Flop
D latch
(master)
D
C
Q
D latch
(slave)
D
C
Q
D
clk
Q
Y
clk
clk’
Y= D
clk’
Y does not change
clk
Q = Y = D

## Slide 17: Simulation of Rising Edge Triggered D Flip-Flop

## Slide 18: D Flip-Flop Symbols
D FF
D
Q
clk
C
Rising edge triggered
D Flip-Flop
D FF
D
Q
clk
C
Falling edge triggered
D Flip-Flop
Characteristic Equation
  Q(t+1) = D
  Y=D

## Slide 19: JK Flip-Flop
Characteristic Equation
  Q(t+1) = JQ’(t) + K’Q(t)
  Y = Jy’ + K’y
J
Q
C
K
J | K | Q(t+1) | Next State
0 | 0 | Q(t) | No change
0 | 1 | 0 | Reset
1 | 0 | 1 | Set
1 | 1 | Q’(t) | Complement
Characteristic Table
J | K | Y | Next State
0 | 0 | y | No change
0 | 1 | 0 | Reset
1 | 0 | 1 | Set
1 | 1 | y’ | Complement

## Slide 20: T (Toggle) Flip-Flop
T
Q
C
T | Q(t+1) | next state
0 | Q(t) | no change
1 | Q’(t) | Complement
Characteristic Equation
  Q(t+1) = T  Q(t) = TQ’(t) + T’Q(t)
  Y = T  y = Ty’ + T’y
J
Q
C
K
T
D
Q
C
T
Characteristic Table
T | Y | next state
0 | y | no change
1 | y’ | Complement

## Slide 21: Analysis of Synchronous Sequential Circuits
Aim:
  Finding the behaviour of the synchronous sequential circuits
  “Behaviour”
    Inputs
    Outputs
    States of the flip-flops
  Finding the Boolean functions of the outputs and the inputs of the flip-flops
      Output and state equations
    state table
    state diagram

## Slide 22: Analysis of Synchronous Sequential Circuits
Current State at time t is stored in an array of flip-flops.
Next State at time t+1 is a Boolean function of Current State and Inputs.
Outputs at time t are a Boolean function of Current State and sometimes Inputs.
Combina-tional
Logic
Inputs
State
Next
State
Outputs
Storage Elements
CLK

## Slide 23: State and Output Equations
They are also called transition equations.
  They show the next state as a function of the present state and the inputs.
Example
D1
D2
D
Q
C
D
Q
C
y1
y1’
y2
y2’
x
z
clk

## Slide 24: State and Output Equations
D1 = ( y1  y2 ) x = Y1
D2 = x y2’ = Y2
z = y1 y2 x
Y1
Y2
D
Q
C
D
Q
C
y1
y1’
y2
y2’
x
z
clk

## Slide 25: Example: State (Transition) Table
1
0
0
0
0
0
0
1
1
0
0
0
0
0
1
0
0
0
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
0
1
0
1
0
0
0
0
0
0
0
0
z
Y2
Y1
x
y2
y1
Output
Next State
Input
Present State
There are 2m+n rows in the state table of a synchronous sequential circuit with m FFs and n inputs.
  Y1 = ?
  Y2 = ?
  z = ?

## Slide 26: Example: State (Transition) Diagram
00
01
10
0/0
1/0
0/0
1/0
1/1
0/0
11
1/0
The state diagram and table give the same information
0/0
Current State |  | Input | Next State |  | Output
y1 | y2 | x | Y1 | Y2 | z
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1

## Slide 28: Analysis of a Synchronous Sequential Circuit with JK Flip-Flops
For a D flip-flop, the state equation is the same as the flip-flop input equation
  Q(t+1) = D
For JK flip-flops, situation is different
  Goal is to find state equations
  Method
    determine flip-flop input equations
    List the binary values of each input equation
    Use the corresponding flip-flop characteristic table to determine the next state values in the state table

## Slide 29: Example: Analysis with JK FFs
Flip-flop input equations
  J1 =xy2 and K1 =x’+ y2
  J2 = x and K2 = 1
J1
K1
J2
K2
J
Q
C
D
Q
C
y1
y2
x
clk
K
J
Q
C
K
1
z

## Slide 30: Example: Analysis with JK FFs
  J1 =xy2 and K1 =x’+ y2
  J2 = x and K2 = 1
0
0
1
0
1
0
0
0
0
1
0
0
0
1
0
0
1
1
1
1
0
1
1
1
0
1
0
1
1
1
1
1
0
1
1
1
0
1
0
1
1
0
0
0
1
0
0
0
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
0
K2
J2
K1
J1
Y2
Y1
x
y2
y1
FF inputs
next state
input
present State

## Slide 31: Example: Analysis with JK FFs
Characteristic equations
  Y1 = J1y1 + K1y1
  Y2 = J2y2’ + K2y2
Flip-flop Input equations
  J1 =xy2 ve K1 =x’+ y2
  J2 = x ve K2 = 1
State equations
  Y1 = xy2y1 + (x’+ y2)y1 = xy2y1 + xy2y1 = x(y2  y1)
  Y2 = xy2’ + 1y2 = xy2’

## Slide 32: State Diagram
00
01
10
0/0
1/0
0/0
1/0
1/1
0/0
11
1/0
0/0
What is the circuit doing?
Present state |  | Input | Next State |  | Output
y1 | y2 | x | Y1 | Y2 | z
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1

## Slide 33: Analysis with T Flip-Flops
Method is the same
Example
T1 = xy0
T0 = x
T1
T0
T
Q
C
D
Q
C
x
clk
T
Q
C
reset
y0
y1

## Slide 34: Example: Analysis with T Flip-Flops
Characteristic equation
  Y0 = T0  y0
  Y1 = T1  y1
Flip-flop Input equations
  T1 = x y0
  T0 = x
State equations
  Y0 = x  y0
  Y1 = x y0  y1

## Slide 35: Mealy and Moore Models
There are two models for sequential circuits
  Mealy
  Moore
They differ in the way the outputs are generated
  Mealy:
    output is a function of both present states and inputs
  Moore
    output is a function of present state only

## Slide 36: Example: Mealy and Moore Machines
36
D
Q
C
x
y
S
clock
reset
C
Mealy Machine
External inputs, x and y, are asynchronous
Thus, outputs may have momentary (incorrect) values
Inputs must be synchronized with clocks
Outputs must be sampled only during clock edges.

## Slide 37: Example: Moore Machines
37
Outputs are already synchronized with clock.
They change synchronously with the clock edge.
T
Q
C
D
Q
C
y1
y2
x
clk
T
Q
C
reset
z

## Slide 38: Example State Diagrams for Moore and Mealy Machines
State Diagram for Mealy Model
State Diagram for Moore Model
0
1
x=1/z=1
x=1/z=0
x=0/z=0
x=0/z=0
1/0
2/1
x=1
x=1
x=0
x=0
x=1
x=0
0/0

## Slide 39: Design Process
Verbal description of desired operation
Draw the state diagram
Reduce the number of states if necessary and possible: s = number of states
Determine the number of flip-flops:
State assignment:
Obtain the encoded state table
Choose the type of the flip-flops
Derive the simplified flip-flop input equations
Derive the simplified output equations
Draw the logic diagram

## Slide 40: Example: Design of a Synchronous Sequential Circuit
Verbal description
  1st Step: we want a circuit that detects three or more consecutive 1’s in a string of bits.
    Input: string of bits of any length
    Output:
      “1” if the circuit detects such a pattern in the string
      “0” otherwise

## Slide 41: Example: State Diagram
Initial
1 came
0/0
1/0
11 came
0/0
1/0
0/0
111 came
1/1
0/0
1/1
2nd Step: Draw the state diagram

## Slide 42: Synthesis with D Flip-Flops 1/5
3rd Step: State reduction
  State 111 and 11 are equivalent, so they can be merged
4th Step: Number of flip-flops
  3 states
  ? flip-flop
5th Step: State assignment
Initial
1 came
0/0
1/0
11 came
0/0
1/0
0/0
111 came
1/1
0/0
1/1
00
01
10
11

## Slide 43: Synthesis with D Flip-Flops 2/5
6th Step: Obtain the state table
1
1
1
0
0
0
1
1
1
0
0
0
0
0
1
0
0
0
0
1
0
0
0
0
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
0
z
Y2
Y1
x
y2
y1
Output
Next State
Input
Present State

## Slide 44: Synthesis with D Flip-Flops 3/5
7th Step: Choose the type of the flip-flops
  D type flip-flops
8th Step: : Derive the simplified flip-flop input equations
  Boolean expressions for D1 and D2
y2x y1 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 1 | 0
D1 = y1x + y2x
y2x y1 | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
D2 = y1x + y2’x

## Slide 45: Synthesis with D Flip-Flops 4/5
9th Step: : Derive the simplified output equations
  Boolean expressions for z
y2x y1 | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
z = y1x

## Slide 46: Synthesis with D Flip-Flops 5/5
10th Step: Draw the logic diagram
D1 = y1x + y2x
D2 = y1x + y2’x
z = y1y2
D
Q
C
R
D
Q
C
R
y1
y2
z
D1
D2
x
clock
reset

## Slide 47: Synthesis with JK Flip-Flops and MUXs
6 shifting lights
= lojik-1
O= lojik-0
Number of states= 6
Number of state variables= 3
Number of Outputs= 6
Number of flip-flops= 3
Number of Inputs= 0

## Slide 48: State Diagram & Table
D0
D1
D2
D3
D5
D4
000
001
010
011
100
101
Y = Jy’ + K’y
J | K | Y
0 | 0 | y
0 | 1 | 0
1 | 0 | 1
1 | 1 | Q’
Y1
Y2
y1
y2
Flip-flop inputs
Next State
Present State
y0
Y0
K1
J1
K2
J2
J0
K0
Outputs
z2
z3
z4
z5
z1
z0
0
0
0
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
k
0
0
k
1
0
k
k
1
k
k
k
0
0
k
1
0
k
1
k
k
k
1
0
1
k
1
k
1
k
1
k
k
k
1
1
1
1
0
1
1
0
0
1
0
0
0
0
0
1
0
1
1
0
0
0
1
0
0
1
1
0
1
1
1
1
1
0
1
0
0

## Slide 49: Inplementation of Flip-Flop Input Equations
y1y0 y2 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | k | k | k | k
J2 = y1y0
y1y0 y2 | 00 | 01 | 11 | 10
0 | k | k | k | k
1 | 0 | 1 | k | k
K2 = y0
y1y0 y2 | 00 | 01 | 11 | 10
0 | 0 | 1 | k | k
1 | 0 | 0 | k | k
J1 = y2’y0
y1y0 y2 | 00 | 01 | 11 | 10
0 | k | k | 1 | 0
1 | k | k | k | k
K1 = y0
y1y0 y2 | 00 | 01 | 11 | 10
0 | 1 | k | k | 1
1 | 1 | k | k | k
J0 = 1
y1y0 y2 | 00 | 01 | 11 | 10
0 | k | 1 | 1 | k
1 | k | 1 | k | k
K1 =1

## Slide 50: Inplementation of Output Equations
y2
y1
z5=y2y1y0+k(y2y1y0+y2y1y0)
y0
0
0
0
y2
y1
z4=y2y1y0+y2y1y0+y2y1y0+k(y2y1y0+y2y1y0)
1
0
y0
0
y2
y1
z3=y2y1y0+y2y1y0+y2y1y0+y2y1y0+y2y1y0+k(y2y1y0+y2y1y0)
1
y0
1
0

## Slide 51: Inplementation of Output Equations
y2
y1
z2=y2y1y0+y2y1y0+y2y1y0+y2y1y0+y2y1y0+k(y2y1y0+y2y1y0)
y0
1
1
0
y2
y1
z1=y2y1y0+y2y1y0+y2y1y0+k(y2y1y0+y2y1y0)
0
1
y0
0

## Slide 52: Inplementation of Output Equations
y2
y1
z0=y2y1y0+k(y2y1y0+y2y1y0)
0
y0
0
0

## Slide 53: Logic Diagram
J2 = y1y0
K2 = y0
J1 = y2’y0
K1 = y0
J0 = 1
K1 =1
Q
D
Q
C
J
Q
C
K
D
Q
C
J
Q
C
K
J
Q
C
K
Q
1
1
clk
Q
Q

## Slide 54: Synthesis with T Flip-Flops 1/4
Example: 3-bit binary counter
012 ...  7  0  1  2
D0
D1
D7
D2
D6
D3
D5
D4
How many flip-flops?
State assignments
D0  000
D1  001
D2  010
...
D7  111
State Diagram

## Slide 55: Synthesis with T Flip-Flops 2/4
State Table
0
0
0
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
0
T0
T1
T2
Y0
Y1
Y2
y0
y1
y2
FF inputs
next state
present state
0
0
0
0
0
0
1
1
0
0
1
1
0
1
0
1
1
1
1
1
1
1
1
1

## Slide 56: Synthesis with T Flip-Flops 3/4
Flip-Flop input equations
y1 y0 y2 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
T2 = y1y0
y1 y0 y2 | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
T1 = y0
T0 = 1

## Slide 57: Synthesis with T Flip-Flops 4/4
Circuit
T2 = y1y0
T1 = y0
T0 = 1
y0
T
Q
C
R
T
Q
C
R
T
Q
C
R
y1
y2
lojik-1
T0
T1
T2
clock
reset

## Slide 58: Unused States
D0
D1
D2
D3
D4
Modulo-5 counter
Present State |  |  | Next State |  | 
y2 | y1 | y0 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0

## Slide 59: Example: Unused States 1/4
y1y0 y2 | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | X | X | X
Y2 = y1y0
y1y0 y2 | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 0 | X | X | X
Y1 = y1’ y0 + y1y0’
= y1  y0
y1y0 y2 | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 1
1 | 0 | X | X | X
Y0 = y2’ y0’
Present State |  |  | Next State |  | 
y2 | y1 | y0 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0

## Slide 60: Example: Unused States 2/4
000
001
010
011
100
101
110
111
Present State |  |  | Next State |  | 
y2 | y1 | y0 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0
Y2 = y1y0
Y1 = y1  y0
Y0 = y2’ y0’
The circuit is not locked type.

## Slide 61: Example: Unused States 3/4
Not using don’t care conditions
Present State |  |  | Next State |  | 
A | B | C | A | B | C
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
BC A | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0
A(t+1) = A’BC
BC A | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
B(t+1) = A’B’C + A’BC’
= A’(B  C)
BC A | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 0 | 0
C(t+1) = A’C’

## Slide 62: Example: Unused States 4/4
Present State |  |  | Next State |  | 
A | B | C | A | B | C
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0
A(t+1) = A’BC
B(t+1) = A’(B  C)
C(t+1) = A’C’
000
001
010
011
100
101
110
111

## Slide 63: Design Example
Design the synchronous sequential circuit which gives “1” as output when the last 4 values from the 1-bit input are 1010.
Example: x= 1010 1011 ise z= 0001 0000
Initial State
1 came
0/0
1/0
10 came
1/0
0/0
0/0
101 came
1/0
0/1
Mealy Machine
00
01
10
11
1/0

## Slide 64: State Table
0
1
0
1
0
0
0
1
1
0
0
0
0
1
0
0
0
1
0
1
0
0
0
0
1
1
1
0
1
1
1
0
1
0
0
1
1
1
0
0
1
0
1
0
0
0
0
0
z
Y2
Y1
x
y2
y1
Output
Next State
Input
Present State

## Slide 65: Verilog Code
module MealyMachine(x,y,clk,rst);
input x,clk,rst;
output y;
parameter IS=0, S_1=1, S_10=2, S_101=3;
reg [1:0] state;
reg y;
S_10: begin
y = 0;
if(x) state = S_101;
else state = IS;
end
S_101: begin
if(x) begin
state = S_1; y =0;
end else begin
state = IS; y =1;
end
end
endcase
end
endmodule
always @(posedge clk)
begin
if (rst) begin state = IS; y = 0;
end else
case (state)
IS: begin
y = 0;
if(x) state = S_1;
else state = IS;
end
S_1: begin
y = 0;
if(x) state = S_1;
else state = S_10;
end

## Slide 66: RTL Schematic

## Slide 67: Timing Diagram
Ideal Case: Delay = 0
Not Ideal Case: Delay  0

## Slide 68: Moore Machine
Initial State
y=0
1 came
y=0
0
1
10 came
y=0
1
0
0
101 came
y=0
1
0
1010 came
y=1
0
000
001
010
011
100
1
1

## Slide 69: Verilog Code
module MealyMachine(x,y,clk,rst);
İnput x,clk,rst;
output y;
Parameter IS=0, S_1=1, S_10=2, S_101=3, S_1010=4;
reg [2:0] state;
reg y;
S_10:
y =0;
if(x) state = S_101;
else state = IS;
S_101:
y =0;
if(x) state = S_1;
else state = S_1010;
S_1010:
y =1;
if(x) state = S_1;
else state = S_IS;
endcase
end
endmodule
always @(posedge clk)
begin
if (rst) state = IS; y = 0;
else
case (state)
IS:
y =0;
if(x) state = S_1;
else state = IS;
S_1:
y =0;
if(x) state = S_1;
else state = S_10;

## Slide 70: RTL Schematic

## Slide 71: Timing Diagram
Ideal Case: Delay = 0
Not Ideal Case: Delay  0